| Name: | Test: | Date: |
| --- | --- | --- |
| Federal Fire Department Certification |
| Certification | Paratech Maxi force Air bags |

| Standard: Utilizing the Paratech Maxi force Air bag System demonstrate the following sequence of events within 5 minutes. 1. Inflate two air bags and disconnect inflated bags from dead-man control per job analysis. 2. Deflate and places system back into service ready position per job analysis. Worth 75 points |
| --- |
| Steps required To Successfully Complete Certification | Successfully Completed |
| 1. Wears required PPE |  |
| 2. Time starts when order is given to inflate two air bags. |  |
| 3. Removes tool case, SCOTT air bottle, and selected bags from apparatus. |  |
| 4. Connects regulator to air supply cylinder and the to dead-man control using black hose. Engages safety lock. |  |
| 5. Connects in-line valves to dead-man control discharges. Valves in open position. Engages safety lock. |  |
| 6. Opens cylinder valve to establish air supply. Opens regulator shut-off. |  |
| 7. Sets pressure regulator to 118 psi. |  |
| 8. Connects colored hoses to in-line valves on dead-man control and to air bags. Engages safety locks |  |
| 9. Inflates desired air bag using “up” control valve. Maximum 30 psi under no load. |  |
| 10. Closes in-line valve at dead-man control and disconnects inflated bag from control valve. Keeping in-line valve and hose connected to air bag. |  |
| 11. Places in-line valve back on dead-man control and opens in-line valve. Deflates air bag using “down” button on dead-man control |  |
| 12. Shuts off air supply at cylinder valve. Disconnects colored hose from in-line valve. Depresses “up” button on dead-man control to bleed air. Time stops. |  |
| 13. Places all equipment back in service ready position on apparatus. |  |
| Successfully Complete | Yes: | No: |
| Comments: |
| Captain: |