## Slide 1: Auto Extrication
FFDSD ACADEMY ORIENTATION 16

## Slide 2: Auto Extrication
Definition
Vehicle Anatomy
  Basic Vehicle Components
  Batteries
  Struts
  High Strength Steel

## Slide 3: Auto Extrication
Vehicle Supplemental Restraint Systems (SRS)
  Airbag-Equipped Vehicles
  Seat Belt Pretensioners
  Passive Roll Bar Systems
Extrication Tools

## Slide 4: Auto Extrication
Vehicle Stabilization
Vehicle Extrication
Alternative Fuel Vehicles

## Slide 5: Auto Extrication
Process of removing accident victims trapped in the wreckage of their vehicles.
Also referred to as vehicle disentanglement

## Slide 6: Auto Extrication
“Golden Hour”
Extrication of victim within 15 minutes is ideal
Sole responsibility of Fire service to extricate trauma patients from their vehicles in a timely and safe manner
Cause no further harm

## Slide 7: Auto Extrication
Newer vehicles designed with safety in mind
  Crumple zones
  HSS, AHSS, and SRS
  Basic idea is to disperse energy around passenger compartment
Learn to “Read the Wreck”

## Slide 8: Auto Extrication Vehicle Anatomy

## Slide 9: Auto Extrication Vehicle Anatomy
Top
  The top of the car is always the roof, even if it is overturned
“A” Post
  Is the vertical structural member of the vehicle which frames in the windshield
  It is located furthest to the front and extends from the dash to the roof

## Slide 10: Auto Extrication Vehicle Anatomy
“B” Post
  Is the vertical structural member of the vehicle which extends from the rocker panel to the roof of the car
  The “B” post is located one post to the rear of the “A” post and provides latching point for front door
“C” Post etc...
  Is the vertical structural member of the vehicle which may frame in the rear window of the vehicle
  On larger vehicles may serve the purpose similar to the “B” post
  As vehicles get larger, so do the number of vertical posts encountered on the vehicle

## Slide 11: Auto Extrication Vehicle Anatomy
“A”
“B”
“C”
“D”
“E”
“F”

## Slide 12: Auto Extrication Vehicle Anatomy
Roof Rail
  The beam that runs perpendicular to, and connects the “A,” “B” and C” Posts
Rocker panel
  The rocker panel is the rigid area of a vehicle between the bottom of the “A” and “B” posts
  Fuel lines run through the rocker panel in some vehicles

## Slide 13: Auto Extrication Vehicle Anatomy
Fender Rail
  Area that runs the top outside edge between the front of the vehicle and the “A” post
  This area is also referred to as the “quarter panel”
Kick Panel
  Area of the vehicle just below the “A” post and forms the rear edge of the quarter panel or fender rail

## Slide 14: Auto Extrication Vehicle Anatomy
Nader Pin
  Attached directly to the “B” post and serves as the latching point for the front doors
  Depending on the number of doors on the vehicle, a Nader Pin may be found on the “C” posts as well
  May also be a hook or loop

## Slide 15: Auto Extrication Vehicle Anatomy
Reinforcement bars
  Designed to give added strength to the doors of a vehicle
  These bars are made of high strength steel and run front to back in vehicle doors
  Placed so the bar will penetrate the post preventing the door from opening in the event of an accident
  Problem for rescuers is that the bar acts like a dead bolt and prevents conventional removal of the door

## Slide 16: Auto Extrication Vehicle Anatomy
Transverse Beam (Magnesium)
  Solid structure found inside the dash board designed to provide lateral (side-to-side) strength of the passenger compartment
  It is also where dashboard components are mounted
  Transverse beam is commonly made of magnesium and can present additional hazards if fire is involved

## Slide 17: Auto Extrication Vehicle Anatomy
Batteries
  Major component of electrical system
  Must locate to de-energize vehicle prior to extrication
  Not always located under hood
  Other possible locations include
    Engine compartment
    Trunk
    Any of the 4 wheel wells
    Under any of the seats
    Under any of the floor boards

## Slide 18: Auto Extrication Vehicle Anatomy
Struts
  Designed to absorb shock, impact, and assist with lifting and stabilizing heavy components
  Typically filled with a compressed gas or liquid
  Most commonly found under the hood, trunk, bumpers, and on hatches or compartment doors

## Slide 19: Auto Extrication Vehicle Anatomy
Struts - Safety concerns
  Under pressure by design
  Cutting one may cause a deadly projectile or explosion
  Can be under extreme pressure after a vehicle accident
  Impinged by fire, can heat up to the point where they can no longer contain the pressures inside, exploding or propelling themselves great distances
Projectile Strut

## Slide 20: Auto Extrication Vehicle Anatomy
Struts
  Bumper Struts
    Most vehicles manufactured after 1974
    Used to create energy absorbing bumpers
    Similar design to those found in struts
    When the energy absorbing pistons are heated or impinged by fire, they can unexpectedly explode or release, launching the bumper or the individual piston great distances
Projectile Strut

## Slide 21: Auto Extrication Vehicle Anatomy
Struts
  Bumper Struts
    Should always approach vehicles at a 45° to 90° degree angle from the front or back
    Keep clear of a potential bumper release during vehicle fires or extrication

## Slide 22: Auto Extrication Vehicle Anatomy
Vehicle Frames
  Two basic frame types
    “Body Over Frame”
    “Unibody”
  Both designs employ plastic components, including plastic skins
    Makes it difficult to gain a purchase

## Slide 23: Auto Extrication Vehicle Anatomy
“Body Over Frame”
  Consists of two steel beams or rails that run the length of vehicle
  Frame provides the attachment foundation for all other components of the vehicle, such as the engine, body, wheels, etc...
  Primarily used in trucks and larger sport utility vehicles
  May still be found in passenger vehicles constructed prior to the 1980’s

## Slide 24: Auto Extrication Vehicle Anatomy
“Body Over Frame”
  Usually heavier
  Tend to hold up better in a collision

## Slide 25: Auto Extrication Vehicle Anatomy
“Unibody”
  Also known as “monocoque”
  Found on most passenger and small sport utility vehicles in production today
  Has no discernible frame rails
  Entire vehicle supports the weight of itself
  The posts, rocker panels, dashboards, roof rails, and sometimes the windows, all work together to provide an intact passenger compartment

## Slide 26: Auto Extrication Vehicle Anatomy
“Unibody”
  Typically made through a process called hydro-forming
    Fluid is pressurized in to a mold creating a formed product with no seams or welds
  For additional strength, a boron steel bar is placed into the open space of the posts and rails
  Strong under normal conditions
  When any part of the body is compromised, rapid failure of the entire vehicle may follow

## Slide 27: Auto Extrication Vehicle Anatomy
(HSS)High Strength Steel
  Used to decrease weight and increase strength
  Poses a challenge for rescuers because hydraulic tools may not be able to cut, bend or push some of these metals

## Slide 28: Auto Extrication Vehicle Anatomy
(HSS)High Strength Steel - Types
  Mild Steel, MS
    (36,000 lbs of tensile strength) This material is within the limits of all our rescue tools and is normally found in fenders, floor panels, quarter panels and rocker panels
  High Strength Steel, HSS
    (50,000 lbs of tensile strength) Also within the limits of our tools and found in hoods, door skins and quarter panels

## Slide 29: Auto Extrication Vehicle Anatomy
(HSS)High Strength Steel - Types
  High Strength Low Alloy, HSLA
    (87,000 lbs of tensile strength) Outside the max force provided by most hydraulic tools. Found in posts, side members, rail strut supports and crumple zones
  Ultra High Strength Steel, UHSS
    (116,000 lbs of tensile strength) This material is outside the working range of most of our tools. These materials are used for posts, reinforcement bars (found in doors) and dash boards of most new vehicles

## Slide 30: Auto Extrication Vehicle Anatomy
(HSS)High Strength Steel - Types
  Advanced High Strength Steel, AHSS
    (203,000 lbs of tensile strength) This material is outside the working strength of all our tools. Also known as Boron steel, it is very hard and brittle. An attempt at cutting this material will result in either the shattering of the material, the shattering of your tool, or no progress at all

## Slide 31: Auto Extrication Extrication Tools
Air Bags
Air Chisel
Bolt Cutters
Cribbing
Flat Headed Axe
Floor Jack (US&R)
Hacksaw
Halligan
Hay Hook
Hydraulic tools (Amkus)
Pick Headed Axe
Pry Bar
Pry Axe
Port-a-Power (Engines)

## Slide 32: Auto Extrication Extrication Tools
Reciprocating Saw or “Sawzall”
Rescue Wrench
Seat Belt Cutter
Sledge Hammer
Stabilization Jacks (US&R 53)
Step Chocks
Utility Rope
Window Punch
Winch (RESCUE 17)

## Slide 33: Auto Extrication Extrication Tools
NAME | USE | WEIGHT | OPENING FORCE | CLOSING FORCE
Power Unit | Power Tools | 100 lbs | N/A | N/A
Cutters | Cutting | 30 lbs | N/A | 60,000 lbs
Speedway Cutters | Cutting | 35 lbs | N/A | 60,000 lbs
30” Ram | Spreading | 27 lbs | 30,650 lbs | 14,400 lbs
40” Ram | Spreading | 33 lbs | 30,650 lbs | 14,400 lbs
60” Ram | Spreading | 43.5 lbs | 30,650 lbs | 14,400 lbs
Spreaders | Spreading | 47.5 lbs | 16,950 lbs | N/A
HURST Hydraulic tools

## Slide 34: Auto Extrication Supplemental Restraint Systems (SRS)
Adds safety to occupants
Adds potential danger to rescuers
1988 1st driver side air bags appeared in passenger cars
2011 some vehicles boast up to 16 airbags

## Slide 35: Auto Extrication Supplemental Restraint Systems (SRS)

## Slide 36: Auto Extrication Supplemental Restraint Systems (SRS)
Driver’s Airbag
Passenger Airbag
Rear passenger airbags stored in the back of the front seats
Side Airbag (Front and Rear)
Impact Curtain, Inflatable Tubular Structure
Knee Airbag
Seat Belt Pre-tensioners
Automatic Roll Bars

## Slide 37: Auto Extrication Supplemental Restraint Systems (SRS) Airbag-Equipped Vehicles
Identifiable by:
  Steering wheel hub
  Verbage:
    “Supplemental Inflatable Restraint”
    “SIR”
    “Air Bag”
    “SRS”
  Vehicle identification number (VIN)
  Placards under hood or on driver’s side windshield pillar
  If unable to determine, always err on the side of safety.

## Slide 38: Auto Extrication Supplemental Restraint Systems (SRS) Airbag-Equipped Vehicles
Rescue with Undeployed Air-bag
  Unlikely to deploy after a crash on its own
  Three things must happen for airbags to deploy
    The vehicle must have speed or be moving. They will not deploy if vehicle is stopped
    There must be an impact on the airbag sensors
    The airbag sensors must detect rapid vehicle deceleration

## Slide 39: Auto Extrication Supplemental Restraint Systems (SRS) Airbag-Equipped Vehicles
Rescue with Undeployed Air-bag
  Even with the aforementioned prerequisites for the activation of air bags, there have been rare cases of inadvertent airbag deployment.
  Can cause severe injury or death
  Employ the “5-10-20” rule

## Slide 40: Auto Extrication Supplemental Restraint Systems (SRS) Airbag-Equipped Vehicles
Rescue with Undeployed Air-bag
“5-10-20” Rule
  Keep all personnel and equipment
    5 inches from the door
    10 inches from the steering wheel
    20 inches from the passenger side dash board

## Slide 41: Auto Extrication Supplemental Restraint Systems (SRS) Airbag-Equipped Vehicles
Rescue with Undeployed Air-bag
  STABILIZE
  DE-ENERGIZE
  EXTRICATE

## Slide 42: Auto Extrication Supplemental Restraint Systems (SRS) Airbag-Equipped Vehicles
Rescue with Undeployed Air-bag
  Stabilize vehicle
  De-energize vehicle
    Disconnect battery cables, negative first
    Cut battery cables, negative first
      Remove about an inch or more
  Extricate

## Slide 43: Auto Extrication Supplemental Restraint Systems (SRS) Airbag-Equipped Vehicles
Rescue with Undeployed Air-bag
  De-energizing
    Roll down windows, move seat back, unlock doors, etc. before de-energizing vehicle
    Turn on 4-ways
    When 4-ways go out, battery is disconnected
    Some capacitors will continue to hold a charge

## Slide 44: Auto Extrication Supplemental Restraint Systems (SRS) Airbag-Equipped Vehicles
Rescue with Undeployed Air-bag
  Peel and peek
    Airbags, compressed gas cylinders, or other SRS components may be dispersed in various locations
    No standard for placement of SRS components
  Peel back plastic and fabric to expose metal frame of vehicle

## Slide 45: Auto Extrication Supplemental Restraint Systems (SRS) Airbag-Equipped Vehicles
Rescue with Deployed Airbags
  Approached as if undeployed airbags until proven otherwise
  STABILIZE, DE-ENERGIZE, EXTRICATE
  “5-10-20” rule
  Victim may have burns on face from airbag deployment

## Slide 46: Auto Extrication Supplemental Restraint Systems (SRS) Airbag-Equipped Vehicles
Seat Belt Pretensioners
  Used to prevent occupants from leaving their seats during a vehicle accident
  Occupants pulled back into their seats so as not to impact the airbag with such a great force
  Concerned with accidental discharge of pyrotechnic component
  Found at the base of either front seat or in the “B” post

## Slide 47: Auto Extrication Supplemental Restraint Systems (SRS) Airbag-Equipped Vehicles
Seat Belt Pretensioners

## Slide 48: Auto Extrication Supplemental Restraint Systems (SRS) Airbag-Equipped Vehicles
Seat Belt Pretensioners
  Found using “peel and peek”
  Do not cut into or apply pressure to these devices
  Remove the victim’s seat belt as soon as practical and safe

## Slide 49: Auto Extrication Supplemental Restraint Systems (SRS)
Passive Roll Bar Systems
  Some convertible vehicles have been designed with hidden roll bars
  Will deploy in a fraction of a second when the vehicle senses a roll past 51° degrees from horizontal
  Most bars will either shoot straight out or hinge up
  Peel and peek, look for markings, may reveal the presence of a passive roll bar system

## Slide 50: Auto Extrication Scene Management Arrival at Scene
Common considerations
  Stabilize
  Utilize vehicle power
  De-energize
  Patient Care
  Peel and Peek
  Extricate

## Slide 51: Auto Extrication Scene Management Arrival at Scene
What is wrong with this picture?

## Slide 52: Auto Extrication Scene Management Size-up
Should include:
  Report on conditions
  Traffic Control
  Identify Hazards
    Electrical issues
    Fire or fuel spill
    Unstable vehicle
    Hazardous materials or cargo
  Number of patients
  Needs/Resources
  Plan

## Slide 53: Auto Extrication Scene Management Special Considerations
At Night
  Illumination is paramount
  Common for unrestrained accident victims to be ejected
    Can be thrown considerable distances
  Search area thoroughly
  Consider using a TIC
  Account for occupants

## Slide 54: Auto Extrication Scene Management Special Considerations
Scene Protection
  Attempt to exit apparatus on the non-traffic side
  Never turn your back to traffic
  Look-outs or Safety officers are helpful if you can’t keep an eye on traffic
  Use caution when using flares
  25 foot Hot Zone (Exclusion Zone) around the vehicle should be maintained
    Only necessary personnel in full PPE

## Slide 55: Auto Extrication Scene Management Special Considerations
Flammable Liquid Control
  Attempt to stop or control any leaking flammable liquids
  Warn personnel about sparks and fire danger prior to beginning extrication
  Have Dry Chemical Extinguisher at the ready
  If it is a large spill request Haz Mat
  “Hot Zone” must be increased to 100 feet when flammable liquids are a factor

## Slide 56: Auto Extrication Scene Management Special Considerations
Electrical Hazards
  Always be assumed to be energized or “hot” when electrical boxes and downed wires are involved.
  Do not attempt to make any extrication attempts, or move any downed power lines
  Wait until confirmation that power is shut down
  Focus on calming the patient and giving them instructions to stay in the vehicle until deemed safe by SDGE or the IC

## Slide 57: Auto Extrication Scene Management Special Considerations
Electrical Hazards
  Vehicle itself can be an electrical hazard
  Part of the initial actions (STABILIZE, DE-ENERGIZE, EXTRICATE)
    Use vehicle power for necessary functions before...
    Vehicle ignition should be turned off
    Batteries disconnected starting with the negative terminal (black)

## Slide 58: Auto Extrication
Operations

## Slide 59: Auto Extrication Operations Stabilization
Second only to scene size-up
Two reasons for Stabilization
  Keep vehicle from moving and further injuring patients or rescuers
  Creates solid platform to perform rescue and extrication operations
Brick vs. Beachball
Bring vehicle off of Suspension by letting air out of tires

## Slide 60: Auto Extrication Operations Stabilization
Older vehicles more resemble a “brick”
Newer vehicles have a more round plastic shell and resemble a “beach ball”

## Slide 61: Auto Extrication Operations Stabilization
“Bricks”
  Square or rectangular surfaces
  Hard exterior shell
“Beach Ball”
  Aerodynamic design
  Rounded
  Easily warped and malleable plastic shells

## Slide 62: Auto Extrication Operations Stabilization
Upright Vehicle
  Place wheel blocks or cribbing on both sides of at least one tire
  Place vehicle in park or in gear and set parking brake if accessible
  Use cribbing or step chocks to make four points of contact on vehicle frame
    Two points per side, under “A” posts behind tire and in front of rear tire

## Slide 63: Auto Extrication Operations Stabilization
Upright Vehicle
  Four points is best, but three points is also good enough
  Operation is the same on one side with the third chock on opposite side beneath the “B” post
  Step chocks can be used...
    Right side up
    Right side up with a wedge
    Upside down

## Slide 64: Auto Extrication Operations Stabilization
Overturned Vehicle
  Cribbing
  Paratech Rescue Struts (US&R 53)
    Tensioned Buttress
  Airbags with cribbing (if necessary)

## Slide 65: Auto Extrication Operations Stabilization
Crib Beds
2x2 Crib Bed
(Max 3:1)
Height to Width
3x3 Crib Bed
(Max 3:1)
Height to Width
Solid Crib Bed
(Max 3:1)
Height to Width

## Slide 66: Auto Extrication Operations Stabilization
Crib Beds
Parallelogram Crib Bed
(Max 1:1)
Height to Width
Triangle Crib Bed (Max 1:1)
Height to Width
Sloped Surface Crib Bed

## Slide 67: Auto Extrication Operations Stabilization
Crib Beds
  4” x 4” dimensional cribbing has a load capacity of 6000 lbs. at each load point
  6” x 6” dimensional cribbing has a load capacity of 15,000 lbs. at each load point
  Crib height is limited to 3 times the width of the crib base or 3:1

## Slide 68: Auto Extrication Operations Stabilization
Crib Beds
  Cribbing corners/load points should overlap by 4” to assure a slow crush type failure
  Bottom layer of crib should be solid when used on soil or asphalt paving to spread the load evenly

## Slide 69: Auto Extrication Operations Stabilization
Vehicles off the Roadway
  Creative cribbing or shoring techniques
  Consider the use of ropes, chains, or winch (US&R 53)

## Slide 70: Auto Extrication Operations Opening/Removing Doors
Try before you pry
Remove Glass
De-energize
Can try to use hand tools, like a Halligan first
  Don’t spend too much time on hand tools
  If hand tools don’t work, switch to power tools

## Slide 71: Auto Extrication Operations Opening/Removing Doors
Removing Glass
  Laminated Glass
    Windshields
  Tempered Glass
    Side and Rear windows

## Slide 72: Auto Extrication Operations Opening/Removing Doors
Removing Glass
  Windshields
    Various methods
      Axe, Pry Axe, Sawzall, Windshield Saw, Halligan
    Protect patient
    Can remove completely or fold down onto the hood

## Slide 73: Auto Extrication Operations Opening/Removing Doors
Removing Glass
  Tempered Glass
    Various Methods/tools
      Roll Down Window, Rescue Wrench, Window Punch, Halligan, Sledgehammer
    Protect Patient
    Clear glass completely

## Slide 74: Auto Extrication Operations Opening/Removing Doors
Create a Purchase
  Use of Hand tools
  Vertical Lift
  Fender Crush
  Enlarging existing purchase

## Slide 75: Auto Extrication Operations Opening/Removing Doors
Create a Purchase
  Hand Tools
    Sledgehammer
    Halligan
    These two tools are primarily used to pound in metal or pry metal out to create a purchase point

## Slide 76: Auto Extrication Operations Opening/Removing Doors
Create a Purchase
  Vertical Lift
    Insert tips of the spreaders between top and bottom of the window frame and spread
    If done over the handle area of the door you should end up with a small opening or purchase point around the area of the Nader pin

## Slide 77: Auto Extrication Operations Opening/Removing Doors
Create a Purchase
  Fender Crush
    Utilized to create a purchase point when attacking the hinges of the front doors
    Use spreaders, pinch the area on the front quarter panel, behind the fender strut housing next to the door hinges
    Crushing movement will create both a purchase point around the upper door hinge and a relief area for a dash roll

## Slide 78: Auto Extrication Operations Opening/Removing Doors
Complete Door Removal From Hinges
  Can access hinges from outside or inside of door
  Force top hinge first via spreader or cutters
  Force Bottom hinge
  Attack Nader pin

## Slide 79: Auto Extrication Operations Opening/Removing Doors
Complete Door Removal From Nader Pin
  Can Access Nader pin from outside of door
  Spread or cut Nader Pin
  Open door toward hinges
  Can leave door in place if access is enough or...
  Remove door by cutting hinges

## Slide 80: Auto Extrication Operations Larger Openings
3rd Door Conversion
“B” Post Blowout
Removing The Roof
Dash Rolls and Pushes

## Slide 81: Auto Extrication Operations
3rd Door Conversion
  For a 2 door vehicle
  Cut “B” Post as high up as possible
  Horizontal relief cut at “B” Post on the Rocker Panel
  Vertical Relief cut next to “C” Post
  Pinch material between cuts with Spreaders and use the leverage to pry the material down
  Place spreaders in the lower “B” post cut and spread the door away and out

## Slide 82: Auto Extrication Operations
“B” Post Blowout
  Used to make a larger workspace in a vehicle
  Two methods
Auto Extrication
Operations

## Slide 83: Auto Extrication Operations
“B” Post Blowout
  Method 1
    Done after the front and rear doors and roof have been removed
    Cut the base of the “B” post to remove it
Auto Extrication
Operations

## Slide 84: Auto Extrication Operations
“B” Post Blowout
  Method 2
    Used if anticipation of removing the “B” post from the beginning of extrication
    Open/pop rear door with the spreaders or cutters
    Cut the “B” post low with the front door still attached and closed
    Place the spreaders in this relief cut and spread the post up and away from the rocker panel
Auto Extrication
Operations

## Slide 85: Auto Extrication Operations
“B” Post Blowout
  Method 2 cont.
    Cut the “B” post as high as possible
    This will now allow you to open the entire side of the car (“B” post, front door, and possibly the rear door) hinging on the front doors hinges
    Lean into the door or use a piece of webbing attached to the door to pull it forward
    If more space is needed remove front door hinges
Auto Extrication
Operations

## Slide 86: Auto Extrication Operations Larger Openings
Removing the Roof
  Remove Windshield and Glass
  Remove or cut seat belts
  Peel and peek
  Cut both the “A” posts first, then work towards the rear posts
  Cut as low as possible on “A” post

## Slide 87: Auto Extrication Operations Larger Openings
Removing the Roof
  Make sure to avoid any pyrotechnics, air bags or seat belt brackets
  Cut high on “B” Post
    Can make a Horizontal or pie cut high on “B” Post
  Cut as low as possible on “C” or last Post
  After all the posts are cut, lift the roof off the car

## Slide 88: Auto Extrication Operations Larger Openings
Roof Fold
  Peel and Peek
  Cut both “A” posts avoiding any SRS
  Pie cut or cut “B” Posts avoiding any SRS
  Vertical Relief cut in front of “C” Post
  Use pry bar to make crease on roof
  Have Firefighters fold roof back along crease

## Slide 89: Auto Extrication Operations Larger Openings
Roof Removal, Vehicle on its Side
  Can use a variety of tools
  Hydraulic cutters, Air Chisel, Sawzall
  Make sure to Stabilize, De-Energize, Extricate
  Remove glass in affected areas
  Protect Patient

## Slide 90: Auto Extrication Operations Larger Openings
Roof Removal, Vehicle on its Side
  Hydraulic Cutters
    Similar process to roof fold
    Cut “A” Post high near roof line, work towards rear of vehicle
    Make horizontal Relief cuts in roof near ground
    Fold down

## Slide 91: Auto Extrication Operations Larger Openings
Roof Removal, Vehicle on its Side
  Air Chisel, Sawzall
    Make purchase into metal
    Cut through sheet metal
    Round Edges
    May have to use cutters to cut through roof supports
    Fold down “skin”

## Slide 92: Auto Extrication Operations Larger Openings
Dash Roll/Push
  Used when victim has become entangled in the dash and/or the steering wheel
  Remove the roof
  Make relief cut in the kick panel, between the hinges, to allow dash to move
  Do not cut the rocker panel, fuel lines may run through there

## Slide 93: Auto Extrication Operations Larger Openings
Dash Roll/Push cont.
  Place a second relief cut on the quarter panel just behind the fender strut
  Place the bottom end of the ram into the lower rear corner of the door opening
  While relief cuts are made cut dash strap (usually located in center of vehicle under dash)
  Crib under the base of the ram below the “B” post so the force is directed into the ground and you do not lose any gain by bending the rocker panel

## Slide 94: Auto Extrication Operations Larger Openings
Dash Roll/Push cont.
  Extend ram until the piston pushes against the top of the kick panel (about dash height where the “A” post meets the dash board)
  Slowly extend until dash is pushed off of victim
  Crib in relief cuts as you go to keep gains
  Cribbing also keep dash in position if tool slips
  Ram can be disconnected from the power unit and left in place to maintain the position of the dash until victim is removed

## Slide 95: Auto Extrication Operations Larger Openings
Dash Jack
  Alternative method for rolling the dash
  Crib under the “A” Post under rocker panel
  Make relief cuts to the kick panel as if planning to use the rams
  Place as deep a cut as you can between the hinges creating both a relief cut and a purchase point for spreading

## Slide 96: Auto Extrication Operations Larger Openings
Dash Jack cont.
  Do not cut the rocker panel, fuel lines may run through panel
  Place another relief cut or pinch forward of the “A” post and behind the fender strut
  Place the spreaders in the cut that was made low on the kick panel and open slowly
  Creates a hinge effect and facilitates removal of the dashboard from the victim

## Slide 97: Auto Extrication Operations Lifting
Used when person/persons are trapped under a vehicle
Various tools and methods can be employed
  Hand tools, Air Bags, Hydraulic tools, Heavy Wreckers
Cribbing as you go is a must

## Slide 98: Auto Extrication Operations Lifting
Lifting a Load - Hydraulic Spreaders
  Place piece of cribbing on ground directly below lift point
  Turn the spreaders vertically
  Open tool so that one tip is in contact with cribbing on the ground and other tip is contacting the lift point
  Slowly begin lifting the vehicle
  Allow time for cribbing

## Slide 99: Auto Extrication Operations Lifting
Lifting a Load - Hydraulic Spreaders cont.
  General rule of thumb
    If you lift an inch, then crib an inch so as to never leave more than one inch of space between the object and the crib bed
    Once the desired height is achieved, the crib bed must be “stuck”
    Command is “Stick It”
    Reply is “Stuck” when wedges are snugged up to vehicle

## Slide 100: Auto Extrication Operations Lifting
Lifting a Load - Airbags
  Air bags can be used to lift a vehicle or heavy object in a combination of ways:
    Single bag lift
    Stacked two bag lift
    Side-by-side two bag lift
  If using air bags on cribbing, use solid base Crib

## Slide 101: Auto Extrication Operations Lifting
Lifting a Load - Airbags
  Use box crib for shoring
  Three rescuer minimum to run Airbag operation
    Safety Observer/Leader
    Airbag Operator
    Cribber

## Slide 102: Auto Extrication Operations Lifting
Lifting a Load - Airbags
  Single bag lift
    Center bag under object to be lifted
    Ensure no sharp edges contacting bag
    Inflate bag slowly checking for possible load shift
    Always crib as object is being raised
      (Rule of thumb: Lift and inch, crib an inch)

## Slide 103: Auto Extrication Operations Lifting
Lifting a Load - Airbags
  Stacked Two Bag Lift
    Larger bag always bottom
    Stacked bags must be centered one on top of the other directly under object to be moved
    Air hoses should be connected to the bags facing different directions
      Prevents air hoses from getting tangled and confusing supply lines

## Slide 104: Auto Extrication Operations Lifting
  Stacked Two Bag Lift cont.
    Ensure no sharp edges contacting bag
    Inflate one bag at a time
    Partially inflate bottom bag first
    Then partially inflate top bag
    Continue sequence until desired height or safe maximum inflation is achieved
    Crib as you go

## Slide 105: Auto Extrication Operations Lifting
Lifting a Load - Airbags
  Side-By-Side Two Bag Lift
    Ensure no sharp edges contacting bag
    Inflate one bag at a time
    Partially inflate one bag
    Partially inflate second bag

## Slide 106: Auto Extrication Operations Lifting
  Side-By-Side Two Bag Lift
    Continue sequence until desired height or safe maximum inflation is achieved
    Crib as you go
    Uneven surfaces should always be cribbed until parallel
    Always crib up to the surface until you can just get bag in
      Retains maximum lift of the bag

## Slide 107: Auto Extrication Operations Lifting
Floor Jack (RESCUE 17)
  Located in belly compartment
  Large throw
  One person to operate
  One person to crib
  Very effective for quick operation
  Limited weight capacity

## Slide 108: Auto Extrication Operations Lifting
Pry Bars
  Last resort (another option)
  Takes manpower
  Coordination is key
  Limited Throw
  Crib as you go

## Slide 109: Auto Extrication Operations Alternative Fuel Vehicles
Vehicle that runs on a fuel other than “traditional” petroleum fuels (gasoline or diesel)
Fuels include ethanol, bio-diesel, natural gas (LNG, CNG), propane, hydrogen, and electricity
Also refers to any technology powering an engine that does not involve solely petroleum
  Hybrid
  Electric vehicles

## Slide 110: Auto Extrication Operations Alternative Fuel Vehicles
Can be used for any number of purposes
  Buses
  Street Sweepers
  Trash Trucks
  Long and Short Haul Trucks
  Fire Engines
  Personel Vehicles

## Slide 111: Auto Extrication Operations Alternative Fuel Vehicles
New Challenges posed
  Noise levels
  Auto-stop function
  Electric Vehicles
Auto Extrication
Operations
Alternative Fuel Vehicles

## Slide 112: Auto Extrication Operations Alternative Fuel Vehicles
Noise levels
  Very quiet when stopped
  Electric vehicles especially
  May fool rescuers into false sense that vehicle is shut down

## Slide 113: Auto Extrication Operations Alternative Fuel Vehicles
Auto Stop
  Shuts down the combustion motor when there is no demand applied to it
  When stopped the words “Auto Stop” should be illuminated on dashboard
  There will be no running motor, no exhaust and no noise
  Any inadvertent push gas pedal will result in the vehicle’s motor engaging and movement
  Properly shut-down prior to patient care or extrication

## Slide 114: Auto Extrication Operations Alternative Fuel Vehicles
Shutting Down a Hybrid Vehicle
  Stabilize Vehicle
  Identify vehicle as potential hybrid
  Place gear shift into PARK
  Set parking brake
  Turn off and remove key
    Remove Smart Keys at least 20 feet from vehicle
    Ensure “Ready” light or “Auto Stop” light is OFF on dashboard
    When “on” and waiting for input from the gas pedal, a light on the dash reads “READY”

## Slide 115: Auto Extrication Operations Alternative Fuel Vehicles
Shutting Down a Hybrid Vehicle
  Ensure that “READY” light is not on before extrication
  De-energize by disconnecting 12 volt DC battery
  Negative terminal first
  Ensure the two battery leads do not recontact battery
  If unable to disconnect battery, remove all fuses from the fuse box
  Attempt to locate the battery disconnect switch for the High Voltage batteries

## Slide 116: Auto Extrication Operations Alternative Fuel Vehicles
Auto Stop on dash
Hybrid Placarding
High Voltage Orange Cables

## Slide 117: Auto Extrication Operations Alternative Fuel Vehicles
Can approach in similar fashion as standard fuel vehicles
STABILIZE - DE-ENERGIZE - EXTRICATE
Stabilize - keep the vehicle from moving
  Bring off of suspension
De-Energize - Shut down the power/brain of the vehicle to its systems
Extricate - Read the wreck
  Stay within the “Golden Hour” for patient care

## Slide 118
Many types of vehicles on the road and they are always evolving
Many different types of vehicle rescues you will encounter
Safety on approach of vehicle
Full PPE
STABILIZE - DE-ENERGIZE - EXTRICATE
Read the wreck, do enough to access the patient
Auto Extrication
Key points

## Slide 119
Do not make the situation worse
Protect the patient
Talk to the patient
Try to get the patient transported to the appropriate facility within the “Golden Hour”
Always keep safety of crews as a priority
Auto Extrication
Key Points

## Slide 120: Auto Extrication Summary
Vehicle rescue incidents requires an individual evaluation and decision on strategy and tactics
No two events will be alike
Consider the incident under control when all victims requiring medical aid have been transported to the hospital
Incident may very well be a crime scene and it is imperative that we disrupt as little as possible
In extrication the experience and training of the crew is paramount to a successful rescue

## Slide 121: Auto Extrication Summary
Train
Train
Train
Try various techniques
Train with various companies and apparatus
Be Safe

## Slide 122: Auto Extrication