## Slide 1: hose

## Slide 2: NFPA Standards- Hose
NFPA 1961- Standard on Fire Hose
NFPA 1962- Standard for care, use and service testing of fire hose; including couplings and nozzles
NFPA 1963- Standard for screw threads and gaskets for fire hose connections

## Slide 3: Types of Hose
Woven Hose
Wrapped Hose
Braided Hose
Rubber-covered Hose

## Slide 4: Hose Construction
Yarns
  Warp- Run lengthwise
    Abrasion resistance
  Filler/Weft- Run “around” the hose
    Burst strength

## Slide 5: Vulcanization Process
Combining the hose jackets
  1. The inner liner is inserted inside the outer jacket.
  2. The rubber liner is inserted inside the outer jackets.
  3. Steam is injected in between the jackets and adheres the rubber liner to the outer jackets.

## Slide 6: Coupling Construction
Sand Cast
  Weakest
  Loose molecular arrangement
Extruded
  Middle in strength
Drop forged
  Strongest
  Dense molecular arrangement

## Slide 7: Types of Couplings
Pin Lug
  Not commonly found, snag hazard
Rocker Lug
  Most common.
Recessed Lug
  Found on Hardline
Extended Handle
  Large diameter couplings

## Slide 9: Parts of a Coupling
Shank
Swivel
Stil Threads
Expansion Ring
Gaskets
Lugs
Higbee Cut & Indicator

## Slide 10: Coupling Inspections
Female Couplings
  G.R.O.T.S.
Male Couplings
  R.O.T.
Identify any gross damage

## Slide 12: Types of Valves
Ball Valves
  Pumper discharges and gated wyes
Gate Valves
  Hydrants
Butterfly Valves
  Large Pump intakes
Clapper Valves
  Siamese appliances and FDC’s

## Slide 13: Valve Devices
  Wye appliances- 1 line into 2
  Siamese appliances- 2 lines into 1
  Water Thief appliances- Variation of Wye
    Used commonly in wildland firefighting

## Slide 14: Hose Fittings
Adapters
  Double Male
  Double Female
Reducers- Follows the flow of water
Increasers- Follows the flow of water
Elbows, Caps and Plugs

## Slide 15: Hose Tools
  Hose Clamp
  Hydrant Wrench
    “One Line”
    Air Horn blast
  Spanner Wrench
  Rubber Mallet
  Straps, ropes and chains

## Slide 16: Hose Loads
  Flat
    4”, 2 ½ “
  Preconnect Flat Load
    1 ¾” in transverse hose bed

## Slide 17: Hose Rolls-
  In-service
    Donut roll
  Out-of-Service- Damaged
    Male is unprotected
  Dirty
    Male is protected

## Slide 18: Hose Lays-
  (2) 200’ 1 ¾” Preconnects- From transverse bed
  2 ½” Preconnect-
  3” Flat Load
  Hydrant lay- “One Line”

## Slide 19: Type 1 Engine Hose Compliment
1 ½” Forestry- Appx. 700’ per engine
1 ¾” Attack- 750’- Preconnects, Bundles High Rise Packs
2 ½” Attack/Supply- 600’
4” Supply- 1000

## Slide 20: Hose Care and Maintenance
  Rolled properly
  Cleaned with water, mild soap if needed
  Brushed
  Rinsed
  DRIED
  Re-rolled or loaded

## Slide 21: Hose Testing
Service tested annually and when suspected damage
  300’ max per discharge at 250 psi for 5 minutes

## Slide 22: Hose Safety Considerations
Open and Close nozzles slowly to prevent water hammer
Use back-up FF’s when needed
Walk out hose before loading
Roll hose before loading if needed
Wear proper PPE’s when working with hose (charged or re-charged)