## Slide 1: Fire Behavior & Modern Fire Behavior

## Slide 2: ENABLING OBJECTIVES
Identify the Science of Fire
Define The methods of Heat transfer
Compare the characteristics of each class of fire
Discuss fire behavior in a structure
Define Legacy Fuels vs Modern Fuels
IDENTIFY MODERN FIREFIGHTING TACTICS

## Slide 3: Why Do we need to understand the science behind fire ?
To better understand and fight fire more effectively
To be able to predict what fire will do in different environments
To be able to change and adapt strategies and Tactics with changing fire conditions and behaviors

## Slide 4: SCIENCE OF FIRE: MATTER
MATTER IS ANYTHING THAT OCCUPIES SPACE AND HAS MASS
CAN UNDERGO PHYSICAL CHANGES DUE TO HEAT AND PRESSURE
Usually there is a transfer of energy whenever there is a physical change to matter

## Slide 5: Science OF FIRE: MATTER
MATTER EXISTS IN 4 STATES
LIQUID
SOLID
GASEOUS
PLASMA - NOT APPLICABLE IN THE FIRE SERVICE

## Slide 6: SCIENCE OF FIRE: MATTER
• MATTER = FUEL
ONLY GASES BURN
MATTER IS CONVERTED THROUGH
  PYROLYSIS
  VAPORIZATION

## Slide 7: SCIENCE OF FIRE: MATTER
PYROLISIS
The chemical decomposition of a substance through the action of heat which results in a lowered ignition temperature.
As solid fuels are heated, combustible materials are driven from the substancE

## Slide 8: SCIENCE OF FIRE: MATTER
VAPORIZATION
The transformation of a liquid to its vapor or gaseous state

## Slide 9: SCIENCE OF FIRE
POTENTIAL ENERGY
STORED ENERGY
CONVERTED TO KINETIC ENERGY WHEN RELEASED

## Slide 10: SCIENCE OF FIRE
OXIDATION
CHEMICAL REACTION INVOLVING OXYGEN WITH OTHER MATERIALS
SLOW – RUST
FAST – COMBUSTION OF METHANE

## Slide 11: SCIENCE OF FIRE
ATMOSPHERIC COMPOSITION
78% NITROGEN
21% OXYGEN
1% TRACE GASES

## Slide 12: SCIENCE OF FIRE
FIRE
Rapid self-sustaining oxidation accompanied by heat and light of varying intensities
ENDOTHERMIC REACTION
CHEMICAL REACTION IN WHICH SUBSTANCE ABSORBS HEAT
EXOTHERMIC REACTION
CHEMICAL REACTION BETWEEN TWO OR MORE MATERIALS THAT CHANGE MATERIALS AND PRODUCE HEAT, FLAMES AND TOXIC SMOKE

## Slide 13: SCIENCE OF FIRE
Combustion
Rapid self sustaining exothermic chemical reaction that usually yields heat and light energy as a result i.e. Fire
Modes of combustion
Flaming Combustion
  Vaporization
Non-Flaming Combustion
  Smoldering

## Slide 14: SCIENCE OF FIRE
Triangle must be intact to create a fire
Three elements required for combustion
  Fuel
  Heat
  Oxygen

## Slide 15: SCIENCE OF FIRE
Most combustion is incomplete and yields smoke and other gasses
Three fuel types
Solid fuels
  Wood, Paper, Cloth and Rubber
Liquid fuels
  gasoline, DIESEL Lubricating Oil
Flammable Gases
  Acetylene
  Hydrogen
  Propane
Notes: Most Combustion is incomplete due to:
• Size and arrangement of fuel
• Contaminants in fuel
• Lack of sufficient oxidize

## Slide 16: SCIENCE OF FIRE
3% needed to allow smoldering
6% or lower cannot support human life
10% or lower respiratory arrest
14% - Combustion will not continue
15% needed to sustain flame
18% - Loss of consciousness
19.5 - 21% - Normal air ranges for human life

## Slide 17: SCIENCE OF FIRE
HEAT ENERGY
MECHANICAL:
  HEAT OF COMPREESION
  HEAT OF FRICTION
ELECTRICAL
  OVER CURRENT/ OVERLOADING
  RESISTANCE
  ARCHING/SPARKING
CHEMICAL
  ENERGY RELEASED AS A RESULT OF A CHEMICAL REACTION IE. COMBUSTION
  CAN BE A SLOW PROCESS OR PROGRESS TO SPONTANOEUS IGNITION
NUCLEAR
  ENERGY RELEASED AS ATOMS SPLIT OR ARE JOINED TOGETHER
  NUCLEAR POWER PLANTS GENERATE POWER AS A RESULT FISSION OF URANIUM

## Slide 18: SCIENCE OF FIRE
FIRE TETRAHEDRON
PRODUCT OF THE FIRE TRIANGLES CHEMICAL REACTION
SELF-SUSTAINING CHEMICAL CHAIN REACTION

## Slide 19: SCIENCE OF FIRE
HEAT TRANSFER
CONDUCTION
  Point-to-point transfer of heat energy from one body to another by means of a heat conducting material
  Direct contact
CONVECTION
  Heat transferred by movement of heated liquids or gases
RADIATION
  Transfers heat across an intervening space

## Slide 20: FIRE BEHAVIOR
FUEL
CLASSIFICATION

## Slide 21: FUEL CLASSIFICATION
CLASS A
ORDINARY COMBUSTIBLES
WOOD
PAPER
PLASTICS

## Slide 22: FUEL CLASSIFICATION
CLASS B
Flammable liquids and gases
Gasoline
Propane
Greases

## Slide 23: FUEL CLASSIFICATION
CLASS C
• Energized electrical
• As soon as equipment, tool, is de-energized, becomes a class A or B fire

## Slide 24: FUEL CLASSIFICATION
CLASS D
Combustible metals
• Zinc
• Magnesium
• Titanium
• Aluminum
• Usually need a specific agent to stop combustion or copious amounts of water

## Slide 25: FUEL CLASSIFICATION
Class K
Cooking media
Greases
Cooking fats
Cooking oils
Uses Saponification to extinguish
Common in commercial Kitchens

## Slide 26: FIRE BEHAVIOR IN A STRUCTURE
PHASES OF FIRE
5 Phases
Ignition
Growth
Flashover
Fully Developed
Decay

## Slide 27: FIRE BEHAVIOR IN A STRUCTURE
Ignition Phase
All 4 Elements of the Fire Tetrahedron Come Together and Combustion Begins
Very Small Fire
21% Oxygen
Low Heat if any at all above Room Temperature

## Slide 28: FIRE BEHAVIOR IN A STRUCTURE
Growth Phase
Fire Plume Forms
Hot Fire Gases Spread upward and outward and Move
Across the Ceiling till they reach the Walls
Depth of Gas Layer Begins to Increase at that Time
16% – 20% Oxygen
1000 to 1300 Degrees F° at CeilinG

## Slide 29: FIRE BEHAVIOR IN A STRUCTURE
Flashover
All surfaces and objects within a space have been heated to their ignition temperature, and flame breaks out almost at once over the surface of all objects in a space.
16% – 20% Oxygen
900 – 1200 Degrees F° Average Room Temperature
Above 1300 Degrees F° at Ceiling
Very Dangerous Situation for Firefighter

## Slide 30: FIRE BEHAVIOR IN A STRUCTURE
Fully Developed Phase
All Combustible Materials in the Room are Involved in the Fire
All Burning Fuels are Releasing the Maximum Amount of Heat Possible.
Large Volumes of Unburned Gases are produced and will Ignite as they find Oxygen

## Slide 31: FIRE BEHAVIOR IN A STRUCTURE
Decay Phase
High Temperatures
1000 Degrees F° at Ceiling
Less than 15% Oxygen

## Slide 32: FIRE BEHAVIOR IN A STRUCTURE
TIME TEMPUTURE CURVES
  TRADITIONAL VS MODERN
  RE-VISIT LATER IN SECTION

## Slide 33: FIRE BEHAVIOR IN A STRUCTURE
THERMAL LAYERING
EXTREME HEAT
MODERATE HEAT
LOW HEAT

## Slide 34: FIRE BEHAVIOR IN A STRUCTURE
Higher heat stays up towards ceiling and expands outward until it hits a barrier and begins to bank down
Things you will see…
Thermal Stratification
Inversion layer
“Mushrooming”
Flame jets or “Jetting”
Spontaneous gas ignition
Rollover or Flame over
Cooler gases and heat levels found closest to ground level
Why it is important to stay low in fire condition

## Slide 35: FIRE BEHAVIOR IN A STRUCTURE
Factors affecting fire growth
Fuel type
Fuel load
Fuel arrangement
O2 concentrations
Flow paths - discussed in further detail in Modern Fire Behavior

## Slide 36: FIRE BEHAVIOR IN A STRUCTURE

## Slide 37: FIRE BEHAVIOR IN A STRUCTURE
FUEL LOAD

## Slide 38: FIRE BEHAVIOR IN A STRUCTURE
FUEL ARRANGEMENT

## Slide 39: FIRE BEHAVIOR IN A STRUCTURE
OXYGEN CONCENTRATIONS
6% or lower cannot support human life
• 10% or lower respiratory arrest
• 14% - Combustion will not continue
• 18% - Loss of consciousness
• 19.5 - 21% - Normal air ranges for human life

## Slide 40: FIRE BEHAVIOR IN A STRUCTURE
OXYGEN CONCENTRATIONS
Related to fire
• 19.5 - 22% fire in ignition and incipient phases
  1500° - 1800° F
• 16 - 18% Free burning phase
  All fuels reach approx. 1100° f
• 14% or less decay phase

## Slide 41: FIRE BEHAVIOR
FLASHOVER, BACKDRAFT, & SMOKE EXPLOSIONS

## Slide 42: FIRE BEHAVIOR
FLASHOVER
All surfaces and objects within a space have been heated to their ignition temperature
• Flame breaks out almost at once over the surface of all objects in a space
• 16 – 20% Oxygen
• 900 – 1200° F Average Room Temperature
• Above 1300° F at Ceiling
• Very Dangerous Situation for Firefighters

## Slide 43
HOW FAR DO YOU HAVE IF YOUR CAUGHT IN A FLASHOVER ?
6 - 8 FEET

## Slide 44: FIRE BEHAVIOR
BACKDRAFT
Instantaneous explosion or rapid burning of superheated gases that occurs when oxygen is introduced into an oxygen – depleted confined space.
Very dangerous situation
Learn to read the signs, the smoke, the building and the fire

## Slide 45: FIRE BEHAVIOR
SMOKE EXPLOSION
A similar phenomenon to a backdraft
Closed compartment suddenly erupts without a sudden opening
The only introduced oxygen is through leakage into the compartment
Can also happen above a vent hole where fuel rich super heated gases escaping a compartment mix with oxygen

## Slide 46: MODERN FIRE BEHAVIOR

## Slide 47: WHY??
212 FIRE FIGHTER LINE OF DUTY DEATHS FROM
2008-2015
122 OF THOSE 212 WERE ON SCENE OF FIRE
COLLABORATION BETWEEN NIST, UL, AND IAFF • MAKE OUR JOB SAFER

## Slide 48: NIST STUDIES LESSONS LEARNED
Controlling ventilation has a significant impact on fire growth
Identifying and controlling flow paths helps to control fire spread
Smoke is unburned fuel
Cooling the environment to help “reset the clock”

## Slide 49: MODERN FIRE BEHAVIOR
LEGACY FUELS
Traditional, natural textiles and building materials
Slower burns
Lower HRR
More time to accomplish fire ground priorities, strategies and tactics

## Slide 50: FIRE BEHAVIOR
MODERN FUELS
Many modern fuels are products of Hydrocarbon fuels.
Plastics
Polymers
Methyl-Ethyl bad stuff

## Slide 51: FIRE BEHAVIOR
MODERN FUELS
Many modern fuels have a much higher HRR
This means they burn hotter and faster
This in turn eats up more Oxygen in the environment
Leading to a premature decay phase
It also pushes Firefighters more to the limits of what our gear can endure and our abilities can overcome

## Slide 52: FIRE BEHAVIOR
MODERN FUELS
Modern fuels are also found in building materials
This means they fail at a faster rate
Usually have less mass and surface area
Leading to early collapse with direct fire impingement
Reduces time frame in which to perform fireground functions.

## Slide 53: MODERN FIRE BEHAVIOR
WHAT IS THE OUTCOME
Understanding what the fire is doing
• THERMAL Inversion layers
• Flow paths
• Ventilation limited fire

## Slide 54: MODERN FIRE BEHAVIOR
NEW TIME TEMPERATURE CURVE

## Slide 55: MODERN FIRE BEHAVIOR
UNDERSTANDING THE TIME TEMP CURVE
Ignition
Growth
Flashover
Free Burning
Decay
Rapid Growth
2nd Flashover event
Free Burning
Decay

## Slide 56: MODERN FIRE BEHAVIOR
UNDERSTANDING THE TIME TEMP CURVE
What caused the second Flashover to occur?
• Rapid introduction of oxygen into fuel rich, oxygen deficient
atmosphere
• Who did that?
• Firefighters

## Slide 57: MODERN FIRE BEHAVIOR
TACTICS
• Door control
• Transitional fire attack
• Heat checks
• Coordinated ventilation
• “Anchor, Darken, Terminate”

## Slide 58: MODERN FIRE BEHAVIOR TACTICS
DOOR CONTROL
Limits oxygen entering structure
Reduces fire growth
Increases timeframe for attack
One person is in charge of door control
Needs to be identified before attack start

## Slide 59: MODERN FIRE BEHAVIOR TACTICS
TRANSITIONAL FIRE ATTACK
Offensive fire tactic
• Cools environment from outside
• Not in IDLH
• “Resets the Clock”
• Do not confuse with transitional mode
  • (moving from offensive to defensive strategies)

## Slide 60: MODERN FIRE BEHAVIOR TACTICS
TRANSITIONAL FIRE ATTACK
10-15 second delivery of water into fire room
• Top corner of window
• Straight stream
• Reposition quickly or have back-up line handle it

## Slide 61: MODERN FIRE BEHAVIOR TACTICS
HEAT CHECKS
Increases SA
• Doesn't allow for attack company to get too deep with fire behind and overhead
• Smoke is unburned fuel
• Stratification
• Looking for droplet return
• Short burst

## Slide 62: MODERN FIRE BEHAVIOR TACTICS
COORDINATED VENTILATION
Keeps firefighter safety
• Do not open up windows or ventilation holes without coordination with attack crews
• Do not start up fans without coordination with attack crews
• Keep vent limited fires from growing too fast

## Slide 63: MODERN FIRE BEHAVIOR TACTICS
“ANCHOR, DARKEN, TERMINATE”
Terms for proper application of water to fire
• Not the circles in a fire room
• Cools the superheated gasses overhead and allows for advance
• Works for advancement of hoseline and fire extinguishment

## Slide 64: ENABLING OBJECTIVES
Identify the Science of Fire
Define The methods of Heat transfer
Compare the characteristics of each class of fire
Discuss fire behavior in a structure
Define Legacy Fuels vs Modern Fuels
IDENTIFY MODERN FIREFIGHTING TACTICS