## Slide 1: Introduction to Hazardous Materials
At the First Responder Awareness (FRA) Level

## Slide 2: The Hazmat Problem
Hazardous Materials are everywhere
  Our modern standard of living requires Haz Mat use and transport
Page B-2
Notes: U.S. DOT regulates over 2,700 substances as “hazardous”. U. S. EPA has over 300 substances on their list of “Extremely Hazardous Substances”.

## Slide 3: The Hazmat Problem
Millions of chemicals in existence
Thousands classified as “hazardous”
Hundreds are “extremely hazardous”
Page B-2

## Slide 4: Elements of Hazmat Problem
Volume of hazardous materials
Variety of hazardous materials
Presence of hazardous materials
The human factor
Page B-2

## Slide 5: Elements of Hazmat Problem
“Events” will happen!
Page B-2

## Slide 6: Three Primary Risks
Life/Health
Environment
Property
Page B-2

## Slide 7: The Hazmat Problem
We can’t eliminate events, but can
  Prepare for events
  Effectively & efficiently respond
  Training helps us do both
Page B-2
Notes: 3

## Slide 8: The Hazmat Problem
Hazmat can kill before you see or smell it
Some events can suddenly get worse
  e.g. BLEVEs
Page B-2

## Slide 9: The Hazmat Problem
Hazmat events are “different”…
  Must respond safely, slowly & methodically
Ms. Gump, your boy’s “different”...
Page B-2

## Slide 10: OSHA Hazwoper Regulation
29 CFR 1910.120
  Federal Regulation
Title 8 California Code of Regs §5192
  California Regulation
  (Identical to fed reg)
Page B-4

## Slide 11: Hazwoper Regulates
Hazardous waste site cleanup
Treatment, storage & disposal facilities
Emergency response to hazmat releases
Page B-4

## Slide 12: Hazwoper Requires Employers To
Plan for response and cleanup
Train employees
Follow basic response requirements
Page B-4

## Slide 13: Focus of this Course
Page B-4

## Slide 14: Hazwoper Training
Reg specifies training for various levels of responders
FRA
FRO
IC
Page B-4

## Slide 15: First Responder’s Role
Primary First Responder role
  Safely and competently respond
  Within appropriate —
    level
    resources
    and capabilities
Page B-4

## Slide 16: First Responder Awareness
OSHA definition
  Likely to witness/discover a release
  Can initiate notifying authorities
  Take no further actions
Page B-4

## Slide 17: First Responder Operations
OSHA Definition
  One who responds to Haz Mat release
    As part of the initial response
    In a defensive fashion
      Doesn’t try to actually stop the release
  Contains release from a safe distance
Page B-6

## Slide 18: Both Levels Have Limits
Equipment
  Lack PPE
Training
  Not trained to stop release
Page B-6

## Slide 19: Hazmat Technicians
Respond to stop the release
Assume a more aggressive role than a first responder
Page B-6

## Slide 20: Hazmat Specialists
Respond with & support technicians
Require a more directed or specific knowledge of various substances
Also act as the site liaison with federal, state & local government
Page B-6

## Slide 21: Incident Commander
Assume control of incident scene
Page B-6

## Slide 22: Others
Skilled Support Personnel
Specialist Employee
Page B-6

## Slide 23: Know Your…
Level
Role
Responsibility and
Limits
Page B-6

## Slide 24: Terms, Definitions & Acronyms
No one universal definition
B-8

## Slide 25: What is “Hazardous”?
Hazardous “Chemical” (OSHA)
  In the workplace
Hazardous “Material” (DOT)
  When transported
Page B-8
Notes: 5

## Slide 26: What is “Hazardous”?
Hazardous “Substance” (EPA)
  None of the above
Hazardous “Waste” (EPA)
  Can’t use it anymore
Page B-8
Notes: 5

## Slide 27: What is “Hazardous”?
Extremely Hazardous Substance
  Strict reporting requirements
Highly Hazardous Chemical
Toxic Chemical
Page B-8
Notes: 5

## Slide 28: Different Laws, Different Terms
Laws passed at different times for different purposes
For FRAs: Don’t worry about it
Hazardous means just that!
Page B-8

## Slide 29: What is “Hazardous”?
UN/USDOT Classification System
  9 hazard classes
  Used worldwide
Explosive
Compressed Gases
Flammable*
Oxidizer
Poison
Radioactive
Corrosive
Misc. Dangerous Substances
Page B-8
Notes: 5

## Slide 30: Hazmat Terms & Acronyms
There are a lot
See list in book
  Page B-9
B-8

## Slide 31: Classification in Transportation
UN & USDOT system
  Uses 9 hazard classes
  Used worldwide & here
B-8

## Slide 32: Hazard Classes w/Examples
Corrosive
Oxidizer
Explosive
Poison
Radioactive
Flammable
Page B-10
Notes: 6

## Slide 33: Explosives (Class 1)
Trinitrotoluene (TNT)
Black Powder
Lead azide
ANFO
PETN
B-10
Notes: ANFO = Ammonium Nitrate Fuel Oil, consists of prilled ammonium nitrate and fuel oil. PETN = pentaerythrite tetranitrate (common explosives used in the construction industry.
8

## Slide 34: Gases (Class 2)
Anhydrous Ammonia
Hydrogen Sulfide
Phosgene
Acetylene
Diborane
B-10
Notes: 10

## Slide 35: Flammable/Combustible Liquids (Class 3)
Gasoline
Alcoholic Beverages
Hydrazine
Toluene
Acetone
Page B-10
Notes: 12

## Slide 36: Flammable Solids (Class 4)
Aluminum phosphide
Naphthalene
Sodium
Barium
Carbon
Page B-10
Notes: 14

## Slide 37: Oxidizers & Organic Peroxides (Class 5)
Red Fuming Nitric Acid
Nitrogen tetroxide
Potassium nitrate
Calcium Nitrate
Fluorine
Page B-10
Notes: 16

## Slide 38: Poisonous & Infections Materials (Class 6)
Hydrazine
Nicotine
Acrolein
Fluorine
Bromine
B-10
Notes: 18

## Slide 39: Radioactive Materials (Class 7)
Uranium Hexafluoride
Thorium
B-10
Notes: 20

## Slide 40: Corrosive Materials (Class 8)
Red Fuming Nitric Acid
Sodium hydroxide
Sulfuric Acid
Hydrazine
Bromine
B-10
Notes: 22

## Slide 41: Misc. Hazardous Materials (Class 9)
Ammonium nitrate fertilizers
Hazardous waste
Wheelchairs
Automobiles
Asbestos
B-10

## Slide 42: Multiple Hazards
Regulations are performance standards
  Material is “hazardous” because it meets DOT definition
  Not all materials neatly fit in definitions
  A substance may meet the definition of more than one hazard class
Page B-12

## Slide 43
Page B-12

## Slide 44: Multiple Hazards
Substances that meet definition of more than one hazard class:
  Classified according to highest hazard class & placarded accordingly
Page B-12

## Slide 45: Subsidiary Hazards
Placards may not indicate all hazards
Page B-12

## Slide 46: Multiple Hazards
Material may not be classified as “hazardous” but, under certain circumstances, be hazardous
  (e.g. ammonia and flammability)
Responders should always think of multiple hazards regardless of how a substance is placarded or labeled!
Page B-12

## Slide 47
Page B-12

## Slide 48: Haz Mat Commons & Typicals
B-12

## Slide 49: Haz Mat Commons
Most common:
  Release: Petroleum products
  Locations: Fixed facilities
  Factor: Collision/Overturn
B-12

## Slide 50: Hazmat Typicals
The typical:
  Responder exposure: Inhalation
  Number of response agencies: Four
  Typical responder: you!
Page B-12

## Slide 51: Tactical Operations Acronym
S
I
N
C
I
A
P
C
P
D
D
D
Page B-14

## Slide 52: Safety
Page B-14

## Slide 53: Isolate and Deny Entry
Page B-14

## Slide 54: Notifications
Page B-14

## Slide 55: Command
“As of now, I am in control...”
A. Haig, 3-30-91
Page B-14

## Slide 56: Identification & Hazard Assessment

## Slide 57: Action Planning
Page B-14

## Slide 58: Protective Equipment
Page B-14

## Slide 59: Containment & Control
Page B-14

## Slide 60: Protective Actions
Page B-14

## Slide 61: Decontamination & Cleanup
Page B-14

## Slide 62: Disposal
Page B-14

## Slide 63: Documentation
Page B-14

## Slide 64: Another Tactical Acronym
B.R.E.A.K