## Slide 1: IDHA and Action Plans: (I.A.)

## Slide 2: IDHA Process
Most critical aspect of a response
  All decisions flow from this
  Regs require IC to do it
  Can’t protect yourself if you can’t identify the problem!
Notes: Protect:
Life,
Environment,
Property.
In that order!

## Slide 3: Hazard Assessment Starts Immediately
Starts with initial discovery/notification
Use recognition clues & common sense
Caution: Initial reports may not be accurate or complete.

## Slide 4: Basic FRA IDHA Process
Identify material(s)
Consult ERG/SDS
Follow employer’s policies

## Slide 5: Basic IDHA Questions
Will something bad happen now?
  Is it on fire?
  Can it explode or burn?
  Is there a gas or vapor present?

## Slide 6: Basic IDHA Questions
Can it hurt me?
  Toxic
  Flammable
  Corrosive
  Radioactive

## Slide 7: Hazard Identification Sources

## Slide 8: Safety Data Sheets
Material Safety Data Sheets (old)
Safety Date Sheets (new)
  Same thing, only different

## Slide 9: SDS - Who
Required by OSHA Hazcom Standard
  29 CFR 1910.1200
  Title 8 CCR 5194

## Slide 10: SDS - Purpose
Informs employees of “hazardous chemicals”
Ensures all chemicals hazards are:
  Evaluated and
  Info is transmitted to employees

## Slide 11: SDS - How
Transmits info via:
  Haz. Comm. Program
  Container labeling
  MSDS/SDS
  Employee training

## Slide 12: SDS
Major source of hazmat info

## Slide 13: SDS Provides Info On…
Physical properties
Hazards of material
Signs & symptoms of exposure
Exposure levels
PPE recommended
Manufacturer contact info

## Slide 14: Who Can Provide SDS
Workplace involved
Manufacturer/distributor
CHEMTREC

## Slide 15: Hazard Identification Sources
DOT placards, labels & markings

## Slide 16: Hazard Identification Sources
Placards and labels
  Stenciled railcars

## Slide 17: Hazard Identification Sources
Placards and labels
  ID # on placards & orange panels

## Slide 18: Hazard Identification Sources
DOT Radioactive labels
  White I (lowest level of activity)
  Yellow II
  Yellow III (highest level of activity)

## Slide 20: Hazard Identification Sources
Shipping papers
“X” marks the spot!

## Slide 21
Proper Shipping Name

## Slide 22
Hazard Class

## Slide 23
ID Number

## Slide 24: Hazard Identification Sources
Pipeline Markers
  Level of hazard
  Name of product

## Slide 25: Hazard Identification Sources
Three sources minimum!

## Slide 26: Hazard Assessment Sources

## Slide 27: NFPA 704 System
Health = Blue
Flammability = Red
Instability = Yellow
Special Hazards = No color (usually white)

## Slide 28: NFPA 704 System
0-4 rating scale for hazards
  4 – severe hazard
  0 – minimal hazard

## Slide 29: Special hazard symbols
COR (corrosive)
POL (polymerization hazard)
OXY (oxygen or oxidizer)
Trefoil (radiation hazard)
W (water reactive)

## Slide 30: Pesticides & Consumer Products
Label must include
  Chemical Name
    Consumer products
  Ingredient Statement
    Pesticides

## Slide 31: Product Label Signal Words
Bad Stuff
Pesticides & Consumer Products
  Danger (highest hazard)
  Warning (moderate hazard)
  Caution (lowest hazard)

## Slide 33: Statement of Principle Hazards
Wording to describe hazards
  Flammable
  Combustible
  Causes Burns
  Etc.

## Slide 35: Precautionary Statements

## Slide 37: CHEMTREC
CHEMTREC
  Chemical Transportation Emergency Center
24 Hour technical information center
Call (800) 424-9300

## Slide 38: CHEMTREC
Can provide SDS
  Over 4 million available
Has access to variety of specialists

## Slide 39: CHEMTREC
Will connect emergency responders with product specialists

## Slide 40: Other Reference Guides
NIOSH Pocket Guide

## Slide 41: Other Reference Guides
Poison Control System

## Slide 43: Other Reference Guides
ChemTel, 3E Company, Infotrac
  24 hour info centers
  Provide SDS from member companies
  Dispatch company response teams
Phone numbers are in ERG

## Slide 44: DOT Emergency Response Guidebook (ERG)

## Slide 45: ERG Purpose
Basic safety tool
Basic identification
Initial actions

## Slide 46: ERG versus SDS
ERG – transportation incidents
SDS – all other incidents
  If current version is available!
ERG
SDS

## Slide 47: ERG Page Colors & Organization

## Slide 48: ERG White Pages (part 1)
Instructions (page 1)
Safety Precautions (pages 2-3)
Hazard Classes (page 4)
Table of Placards (pages 5-7)

## Slide 49: ERG White Pages (part 1)
Railcar & Road Trailer ID (pages 8-9)
Intermodal Container ID # (pages 10-13)
Pipeline ID & Info (pages 14-19)

## Slide 50: ERG Yellow-Bordered Pages
Materials listed by ID number

## Slide 52: ERG Blue-Bordered Pages
Materials listed by name

## Slide 54: ERG Orange-Bordered Pages
Number guide pages

## Slide 56: ERG Green-Bordered Pages
Isolation & Protective Actions
  Toxic Inhalation Hazards
  Water Reactive Substances
  Six Most Common Substances

## Slide 60: ERG White Pages (part 2)
Response Info
BLEVE Safety Precautions
Glossary

## Slide 62: ERG—Good But Limited
Classification of hazard
Guides — “most essential guidance”
Isolation/evacuation distances — guides
Use table of placards only if no ID
Intended use
  “initial phase”

## Slide 63: ERG Specialized Info
“P”: polymerization hazard
Dangerous Water–Reactive Materials
Guide 111

## Slide 64: ERG Caveats
Distances are guides
Use table of placards if you can’t ID material
Intended use
  Transportation-related incidents
  Initial phase of incident

## Slide 65: ERG Use
So let’s use it!
ERG

## Slide 66: What Should This Stuff Not Do?
Notes: Guide 148 – Don’t let it warm up.

## Slide 67: What’s This?
Which guide do you use?
Notes: 1649 = Motor fuel anti-knock mixture. Guide 131

## Slide 68: What are the hazards?
Notes: Toxic (very) and Flammable (highly)

## Slide 69: What’s the Initial Isolation Distance?
Notes: 200 feet. Table 3. It’s an agricultural nurse tank.

## Slide 70: What Guide Page?
Notes: Page 5 of the ERG: “If multiple placards point to more than one guide, initially use the most conservative guide(i.e., the guide requiring the greatest degree of protective actions).” In this case, that would be the Flammable placard.

## Slide 71: What if it Gets Wet?
Notes: Table 2 Green-bordered pages. Gives off hydrogen fluoride.

## Slide 72: Protective Action Distance?
Small spill
At night
Notes: Table 1. Green-bordered pages. 0.2 miles.

## Slide 73: Container Stress & Behavior

## Slide 74: Container Stress & Behavior
Hazmats are released when container fails
  Failure can be minor or catastrophic
  Nature of failure determines potential harm
    Kingman BLEVE vs. Tokyo Sarin

## Slide 75: Hazmat Release Process
Stress on container
Container weakens & fails
Material released
Material disperses

## Slide 76: Hazmat Release Process
Hazard to you depends what step the process is on when you arrive!

## Slide 77: Types of Container Stress
Thermal
  Hot or cold
Mechanical
Chemical

## Slide 78: Evaluating Container Stress
Type of stress?
What will container do?
When will it do it?

## Slide 79: Types of Container Failure
Catastrophic
Fracture
Puncture
Degradation

## Slide 80: Types of Product Dispersion
Instantaneous release
  Spreads in all directions
  Gases/vapors can ignite immediately

## Slide 81: Types of Product Dispersion
Rapid release
  Spreads downwind/downstream

## Slide 82: Types of Product Dispersion
Slow release
  Spreads slowly downwind/downstream

## Slide 83: BLEVE
Cause – Thermal stress on container
  Stress weakens container
  Container breeches
  Near-instantaneous release

## Slide 84: BLEVE
Hazards
  Flying debris

## Slide 85: BLEVE
Hazards
  Large fireball

## Slide 86: BLEVE
Timeframe
  Less than 10 minutes

## Slide 87: Assessing Hazards
If the container fails what will the material do to you?
  Will it explode?
  Will it burn?
  Will it hurt you some other way?

## Slide 88: How Can You Tell?
What are the material’s properties?

## Slide 89: Physical Properties
Properties determine hazard & behavior
Hazard & behavior determine response

## Slide 90: What Properties Tell Us It Will Explode Or Burn?
Boiling Point (BP)
Flash Point (FP)
Ignition Temperature (IT)
Flammable Range (FR)

## Slide 91: Flammable Range
At what concentration will the material burn?
Concentration within the flammable range - material could burn.

## Slide 92: What Else The Properties Tell Us
Will it be a solid, liquid or gas?
  Vapor pressure
  Boiling point
  Freezing/melting point

## Slide 93: Vapor Pressure
How quickly will it evaporate?

## Slide 94: Boiling Point
Will it be a solid, liquid or gas?
Only gases and vapors burn!
Boiling Point
Freezing Point
32° F
212° F

## Slide 95: Flash Point
When will it give off enough vapors to ignite in air?

## Slide 96: Will It Sink Or Float?
VD - Vapor Density (in air)
SG - Specific Gravity (in water)

## Slide 97: Will It Dissolve In Water?
Solubility
  0-100%

## Slide 98: Is It Corrosive?
pH - Acidity/Alkalinity

## Slide 99: How Else it Can Hurt You
Asphyxiation
  e.g. CO2, Nitrogen, Argon, etc.
Carcinogenesis
  e.g. Asbestos, Carbon Tetrachloride etc.

## Slide 100: Is It Radioactive?

## Slide 101: Ionizing Radiation

## Slide 102: Types of Ionizing Radiation
Alpha

## Slide 103: Types of Ionizing Radiation
Beta

## Slide 104: Types of Ionizing Radiation
Gamma

## Slide 105: Types of Ionizing Radiation
Neutron

## Slide 106: Protection Against Radiation

## Slide 107: Is It Toxic?

## Slide 108: Definitions
Toxicology
  Study of adverse systemic effects of chemicals
  Not just the study of poisons. Many substances can be toxic but aren’t classed as poisons!

## Slide 109: Definitions
Poison
  Produces illness or death
  When taken in small quantities

## Slide 110: DOT Requirements
LD50 less than 50 milligram per kilogram of body weight
Placards
  Poison Gas 2
  Poison 6.1
  Poison 6.2

## Slide 111: Limits of Toxicology
Most exposure levels based on animal tests
Test results with animals often different than results with humans

## Slide 112: Assessing Toxicity
Measures of toxicity
There are many
Sources of information on toxicity
  NIOSH Pocket Guide
  Safety Data Sheets (SDS)

## Slide 113: Measuring Toxicity
Tools are available
  Many measure chronic exposure only
  May not applicable to emergency response

## Slide 114: Measuring Toxicity
IDLH
  Immediately Dangerous to Life & Health
TLV™
  Threshold Limit Value
STEL
  Short Term Exposure Limit
Notes: IDLH — Immediately Dangerous to Life & Health;
TLV™ — Threshold Limit Value (guides) – Time Weighted Average. Exposure limit recommended by the American Conference of Governmental Industrial Hygienists (ACGIH). Level to which nearly all workers may be repeatedly exposed without adverse effect. Time weighted average. 8 hour workday. 40 hour workweek. Derived for the protection of healthy, adult male workers.
STEL — Short Term Exposure Limit. Exposure limit recommended by the American Conference of Governmental Industrial Hygienists (ACGIH). All workers should be able to withstand up to four exposures per day at this concentration with no ill effects (if TLV®-TWA not exceeded). Applied to supplement the TLV®-TWA when there are recognized acute effects from a substance whose toxic effects are primarily of a chronic nature.Time weighted average. 15 minutes. 8 hour workday. 40 hour workweek.

## Slide 115: Measuring Toxicity
PEL
  Permissible Exposure Limit
MLD
  Minimum Lethal Dose
ERPG
  Emergency Response Planning Guide
Notes: PEL — Permissible Exposure Limit (law). Legal limit for exposures in the workplace. OSHA/CALOSHA regulation. Majority adopted from TLV’s. (CALOSHA PEL’s usually more up to date.)Uses time weighted averages, short-term exposure limits and ceilings.
LD/LC 50 — Lethal Dose/Lethal Concentration 50%. Concentration level at which 50 percent of the test animals died when exposed by inhalation for a specified time period.Standard measurement used by toxicologists. Dose is usually given in milligrams per kilogram of body weight of the test animal.

## Slide 116: Measuring Toxicity
LD/LC 50
  Lethal Dose 50%
  Lethal Concentration 50%
PPM/MgM3
  Parts Per Million
  Milligrams Per Cubic Meter

## Slide 117: Dose-Response Relationship
Effect depends on the dose
Dose increases – severity of effect increases
Severity of effect depends on duration of exposure

## Slide 118: Routes of Entry & Preventing Exposure
Inhalation - you breath it
  Isolate and deny entry
  Wear SCBA
  Just stay away!

## Slide 119: Routes of Entry & Preventing Exposure
Ingestion - you eat it
  Isolate and deny entry
  Don’t eat, smoke, drink at incident scene

## Slide 120: Routes of Entry & Preventing Exposure
Absorption - soaks through skin
  Isolate and deny entry
  Wear proper PPE
  Decon any exposure

## Slide 121: Routes of Entry & Preventing Exposure
Injection - puncture wound
  Isolate and deny entry
  Wear proper PPE
  How can this happen?

## Slide 122: Remember!
Vapor/gas may be odorless, colorless & tasteless!
You may be exposed before you know it!
Approach safely - UUU
Wear PPE

## Slide 123: Causes of Exposure
Approaching downwind
Wind shifts
Not wearing protective clothing

## Slide 124: Acute vs. Chronic
Exposure
  Acute: short-term, limited,one time
  Chronic: long-term, repeated, continuous

## Slide 125: Acute vs. Chronic
Effects
  Acute: may not show immediately
  Chronic: not detectable for years. May differ from acute effects

## Slide 126: Toxicology Variables
Kind of Hazardous Material
Route of exposure
Dose (concentration) received
Duration & frequency of exposure
Notes: Reactions to a substance may depend greatly on the following:

## Slide 127: Personal Tolerances & Variables
Age
Medical history
Gender
Personal habits

## Slide 128: Variables & Hazard Assessment
Many variables affect IDHA
May influence behavior of material

## Slide 129: Variables & Hazard Assessment
Location can influence dispersion
  Stuff goes downhill
  Buildings can trap and/or redirect airborne contaminants

## Slide 130: Variables & Hazard Assessment
Time of day can affect:
  Evaporation rate
  Flammability
  Reactivity

## Slide 131: Variables & Hazard Assessment
Many properties vary with temperature
Heat makes things worse!

## Slide 132: Variables & Hazard Assessment
Weather
  Gases/vapors will usually go downwind
  Vapor clouds can take longer to disperse in cold weather

## Slide 133: Variables & Hazard Assessment
Basic nature of material
Type/size of release
Condition of container

## Slide 134: Variables & Hazard Assessment
Reactivity
May be difficult to predict results
  See Table 2 of ERG Green Pages

## Slide 135: Bottom Line…
Same material
Different variables
Different response

## Slide 136: There Is No Cookbook
Use your head!

## Slide 137: Managing Risk
What will it do?
Where will it go?
What will it hurt?

## Slide 138: What Will It Do?
Will it do it right now?
Will it hurt me?

## Slide 139: Managing Risk
If something bad can happen, how do we manage that risk?

## Slide 140: Risk Management Process
Identify hazards
Assess the risk
Identify your options
Evaluate risk vs. gain
Monitor and re-evaluate situation
Notes: Non-emergency risk management looks at the hazards common to all workplaces.
Pre-emergency risk management activities take place prior to the emergency.
Emergency risk management activities take place during the incident.

## Slide 141: Assessing Risks
What is the potential severity?
What is the probability it will happen?
What is the potential exposure?

## Slide 142: Rating Risks
Low
Moderate
High
Unacceptable

## Slide 143: Low Risk
Small quantities
Inert solid materials
Undamaged container

## Slide 144: Moderate Risk
Smaller quantities
Low vapor-pressure liquid materials
Undamaged/slightly damaged container

## Slide 145: High Risk
Large quantities/multiple containers
Low vapor-pressure liquids or gases
Slightly/moderately damaged container

## Slide 146: Unacceptable Hazmat Risk
Larger quantities and/or gas cylinders involved
High vapor-pressure liquids, gases, explosives and/or reactive materials
Visibly stressed container and/or flame impingement on a gas cylinder

## Slide 147: Unacceptable Hazmat Risk
An unacceptable risk here is:

## Slide 148: Action Planning
Develop objectives and plan
  Objective – informal, from ERG
  Plan – unwritten, follow ERP

## Slide 149: Formal Action Planning
Incident progresses – use written plan
  Incident Action Plan
  Site Safety Plan
FRO should know and follow both

## Slide 150: Components of Action Plan
ID problem
Assess hazards
ID the resources available
Use resources to solve problem

## Slide 151: Sources of FRO Plan Info
ERG Guide pages
SDS recommendations
Employer guidelines

## Slide 152: Basic FRO Actions
Isolate & deny entry
Acceptable risk present
  Containment and protective actions
Unacceptable risk present
  Isolate and deny entry only

## Slide 153: Action Planning for Rescue
ID the hazard
Assess risk

## Slide 154: Risk Assessment & Rescue
Acceptable risk – rescue
Unacceptable risk – no rescue

## Slide 155: Questions?