## Slide 1: Decon, Disposal, Documentation

## Slide 2: Primary FRO Actions
S.I.N.C.I.A.P.C.P. and…
D.D.D.
J-2
Notes: Safety, Isolation, Notifications, Command, IDHA and Action Plans, Protective equipment; Containment and Protective actions.
Note “other” FRO actions within safety and resource capabilities: Conduct Decon as needed; wait for clean-up Company and proper Disposal; and keep Documentation for later records and reports.
Block focuses on Decon, Disposal and Documentation.

## Slide 3: Response Actions
Conduct decon
Ensure clean-up and proper disposal
Keep documentation
D.D.D.
J-2

## Slide 4: Decontamination
Removing or neutralizing contaminants
  Personnel
  Equipment
J-2

## Slide 5: Types of Decon
Responder
  For personnel working in control zones
  Normally done by hazmat team
Emergency
  Normally done by first responders
J-2

## Slide 6: Responder Decon
J-2

## Slide 7: Emergency Decon
Urgent, field expedient process
Use any available water source
Intended for exposed persons displaying symptoms
Normally done by first responders
J-2

## Slide 8: Emergency Decon
J-2

## Slide 9: Minimizing Exposure & Contamination
Follow basic safety guides
Establish & observe control zones
Ensure all follow above
J-2

## Slide 10: Who, What, When & Why
Why: Prevent escalation of problem
  Exposure: it might be on you
  Contamination: it is on you
J-4

## Slide 11: Degree of Contamination
Amount of material on you
Length of time it’s on you
Concentration of material
Physical state of material
Ambient temperatures
J-4

## Slide 12: Who, What, When & Why
When: Anytime you suspect contamination
  Material is visible
  Victim complains of pain, odor, etc.
  Victim was near release
J-4

## Slide 13: Warning!
Many haz mats are odorless, colorless and tasteless
Acute effects may not show up immediately
You may not be able to confirm exposure/contamination
J-4

## Slide 14: Who, What, When & Why
Who/What: People & equipment
  Victims
  Responders
  Equipment
  Structures
J-6

## Slide 15: Who, What, When & Why
Who usually does decon:
  FRO’s (properly trained & equipped)
  Tech’s and Specialists via Decon Team
How to decon: No absolute methods
  Only general guides
J-6

## Slide 16: Performing Decon
Physical removal
Chemical removal
Emergency decon
J-6

## Slide 17: Performing Decon
Procedures follow logical order
Go from “dirty” to “clean”
Check your plan
Dirty
Clean
Filthy
J-6

## Slide 18: Protective Clothing
Same level as entry team
May be one level down
  Degree of hazard
  Amount of contamination
  Length of exposure
J-6

## Slide 19: Consequences of No Decon
J-6
Acute/Chronic health effects
Problem gets bigger
Death!

## Slide 20: Emergency Decon
Anytime you suspect contamination
Use common sense
  Life risk
  Level of exposure
J-8

## Slide 21: Emergency Decon
Guidelines
  In least environmentally sensitive area
  Clothes off
  Water on
J-8
Notes: Move the victim to a safe refuge, preferably the least environmentally sensitive area, and use copious amounts of water to flush off gross contamination.
Remove all contaminated clothing (including underwear). Note: Victims will usually be more cooperative if you give them something to cover themselves with before you hose them down (e.g. orange Caltrans trash bag).
Flush victim again with copious amounts of water.

## Slide 22: Emergency Decon
Use copious amount of water
  Copious=more than you have used
Remove all clothing from victim
  Including undergarments
J-8

## Slide 23: Emergency Decon
Avoid the following:
  Brushes & abrasives
  Hot water
  Decon solutions
J-8

## Slide 24
J-8

## Slide 25: Emergency Decon Precautions
Remove clothing
  May have to cut off
Avoid contact w/clothing
Segregate contaminated clothing
J-8

## Slide 26: Emergency Decon Precautions
Ensure privacy of victim(s)
  Barriers/temp garments
  Segregate by gender
J-8

## Slide 27: Emergency Decon
Medical considerations
  Decon prior to transport
  Protect equipment from contamination
  Segregate contaminated material
J-8

## Slide 28: Decon Roles & Responsibilities
Must have emergency response plan
Plan must include provisions for decon
J-10

## Slide 29: Decon & ICS
J-10

## Slide 30: Decon Unit Leader
Supervises Decon Unit
J-10

## Slide 31: Decon Unit Leader
Establish Decon Corridor
ID contaminated people/equipment
Supervise Decon Unit
J-10

## Slide 32: Decon Unit Leader
Control movement in CRZ
Coordinate transfer of patients
May use FROs as decon team
  If properly trained
J-10

## Slide 33: Funding & Disposal
J-12

## Slide 34: Disposal Requirements
Haz Mat incidents create haz waste
  “Waste” = material that you can’t re-use
J-12

## Slide 35: “Hazardous Waste”
Toxic
Reactive
Ignitable
Corrosive
J-12

## Slide 36: “Hazardous Waste”
Toxic
Reactive
Ignitable
Corrosive
J-12

## Slide 37: “Hazardous Waste”
Toxic
Reactive
Ignitable
Corrosive
J-12

## Slide 38: “Hazardous Waste”
Toxic
Reactive
Ignitable
Corrosive
J-12

## Slide 39: Disposal Requirements
Strict legal requirements
Track from cradle to grave
You must know them and follow them
  Regs apply to government agencies also!
J-12

## Slide 40: Disposal Requirements
“Flushing Haz Mats Away”?
J-12

## Slide 41: Funding Requirements
Funding and “Responsible Party”:
  Accepts clean-up duty
  Gives clean-up high priority
  Conducts cleanup adequately
Funding begins with and ends with RP
J-14

## Slide 42: Government Funding
Local agencies fund clean-up if:
  No responsible party identified
  Responsible party —
    Refuses or
    Does inadequate clean-up
J-14

## Slide 43: Government Funding
“State Superfund” may pay if:
  Threat to life
  No responsible party or local funding
  Must get pre-authorization
    You have to ask!
J-14

## Slide 44: Government Funding
Primary state funding agencies:
  Dept. of Toxics Substances Control (DTSC)
  Dept. of Fish and Game
  Caltrans
J-14

## Slide 45: Federal Funds
Access via Federal On-Scene Coordinator (FOSC)
Call NRC at (800) 424-8802
J-14

## Slide 46: Federal Funds
“Superfund”
  Won’t fund removal of petroleum products
  Only FOSC rep can obligate funds
$
$
J-14

## Slide 47: Federal Funds
Oil Spill Liability Trust Fund
  “Oil” only
  Spill in or threatens “navigable” waterway
  FOSC or State rep may obligate funds
J-14
Notes: Oil = animal, mineral or vegetable.
“Navigable” waterway = everything from the Pacific Ocean to dry creek beds and storm drains.
DFG has authority to directly spend money from this fund.

## Slide 48: Documentation & Reporting
Role of FRO in documentation
  Capture key initial info (may only get one chance to do this)
Use ICS-214
J-16

## Slide 49: Reasons for Documentation
Cost recovery
Exposure records
Training records
Future lawsuits & investigations, etc.
J-16

## Slide 50: Components of Documentation
Date, time and location
Names of all response personnel
  And exposure times!
Incident conditions, observations and statements
J-16

## Slide 51: Components of Documentation
Chemical names, weather conditions, release factors
Actions taken, resources used, costs incurred
J-16

## Slide 52: Components of Documentation
Casualties, sample data, etc.
Statements & Observations of witnesses
Diagrams, photos, video, samples
J-16

## Slide 53: Hazmat Reports
CHP 407E
CFIRS
Agency’s report
Responsible party
J-16

## Slide 54: Chemical Exposure Records
Keep exposure records!
  Employer must keep for 30 years
All responders: keep own copies
Loren Shelton
J-18

## Slide 55: Chemical Exposure Records
Date, time and location of incident
Chemical name
Type, concentration and duration of exposure
Decon or medical aid given
J-18

## Slide 56: Chemical Exposure Records
They are there to protect you!
J-18